Light-Duty Hybrids Available Now & in Immediate Future:*

|  | Toyota Prius Gen 1 | Honda Civic | Honda Insight | Ford Escape | GM Silverado & Sierra, Gen 1 | Toyota Prius Gen 2 |
| --- | --- | --- | --- | --- | --- | --- |
| Model Year | 2003 | 2003 | 2003 | 2005 | 2004 | 2004 |
| EPA Size Class1 | Compact Sedan | Compact Sedan | Two seater | Compact SUV | Fullsize Pickup | Midsize Sedan |
| EPA Adjusted MPG City/Hwy2 | 52/45 | 48/47 | 57/56 | 35-40/30 | Around 18 | 59/5116 |
| Combined MPG15 | 48.85 | 47.55 | 56.55 | 35.5 | Around 18 | 55.4 |
| Hybrid Technology: |  |  |  |  |  |  |
| Idle Turn Off | Idle Turn Off9 | Idle Turn Off7 | Idle Turn Off8 | Idle Turn Off1 | Idle Turn Off1 | Idle Turn Off10 |
| Regenerative Braking | Regenerative Braking9 | Regenerative Braking7 | Regenerative Braking8 | Regenerative Braking1 | Minimal Regen Braking1 | Regenerative Braking10 |
| Electric Only Drive | Electric Only Drive9 | No7 | No8 | Electric Only Drive1 | NO | Electric OnlyDrive10 |
| Drivetrain Type3 | Series/Parallel | Parallel | Parallel | Series/Parallel | Parallel | Series/Parallel |
| Downsized Engine | Downsized Engine9 | Downsized Engine7 | Downsized Engine8 | Downsized Engine1 | NO | Downsized Engine10 |
| Emissions: |  |  |  |  |  |  |
| Rating4 (Select Availability) | SULEV | SULEV | SULEV | SULEV/AT-PZEV |  | SULEV/AT-PZEV |
| Rating4 (Nat’l Availability) | ULEV | ULEV | LEV, BIN 5 |  |  | Tier 2, Bin 3 |
| EPA Air Pollution Score5 | 7 ULEV; 10 SULEV | 7 ULEV | 6 LEV; 8 BIN 5; 10 SULEV |  |  |  |
| Annual Tailpipe CO218 | 5,944 lbs | 6,107 lbs | 5,135 lbs | As low as 8,180 lbs | Around 16,133 lbs | 5,242 lbs |
| Annual CO2 Emissions6 | 7,369 lbs | 7,571 lbs | 6,366 lbs | As low as 10,141 lbs | Around 20,000 lbs | 6,498 lbs |
| Total Annual GHG Emissions1, a | 6 tons | 6 tons | 5 tons |  |  |  |
| Power |  |  |  |  |  |  |
| Gas Engine1 | 4 cyl; 1.5L; 70hp9 | 4 cyl; 1.3L; 85hp7 | 3 cyl; 1.0L; 65hp8 | 4 cyl; 2.0L; 130hp1 | 8 cyl; 5.3L; 285hp (est.) 11 | 4 cyl; 1.5L; 78hp10 |
| Electric Motor | 44hp9 | 13.4hp7 | 13.4hp8 | 87hp1 |  | 67hp10 |
| Est. Combined hp | 98hp9 | 93hp7 | 71hp8 | 200hp1 |  | 106hp10 |
| Battery | 274V Ni-MH9 | 144V Ni-MH7 | 144V Ni-MH8 | 300V Ni-MH1 | 36V lead-acid1 | Ni-MH |
| CLEAR ACT (S. 505) |  |  |  |  |  |  |
| Technology Tax Credit17 | >30%; $1000 | 10%-20%; $500 | 10%-20%; $500 | >30%; $1000 |  | >30%; $1000 |
| Performance Tax Credit17 | $1500 | $1500 | $1000 | $1500 |  | $2000 |
| Other Notes | 1st HEV to be mass produced; the HEV of choice in fleets |  | Ultra-lightweight aluminum body |  | Generator capabilities1 Integrated starter generator system | “drive-by-wire” (more electronic systems, less mechanical) |

*This chart includes the best available information to date based on automaker announcements.  Actual delivery dates and specifications of any of the models discussed here are subject to change.

|  | Saturn VUE | Lexus RX33016 | Toyota Highlander16 | Toyota Sienna16 | Dodge Ram16 | Chevrolet Equinox16 | Ford Futura |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Model Year | No longer scheduled for release | 2005 | 2005 | 2005 | 2005 (?) | 2007 | 2006 - tbd |
| EPA Size Class1 | Compact SUV | Compact SUV | Midsize SUV | Minivan | Full-size Pickup | Compact SUV | Midsize Sedan |
| EPA Adjusted MPG City/Hwy2 | Up to 40 | Up to 40 |  |  | Up to 18 |  |  |
| Combined MPG15 | Up to 40 | Up to 40 |  |  | Up to 18 |  |  |
| Hybrid Technology: |  |  |  |  |  |  |  |
| Idle Turn Off |  | Idle Turn Off | Idle Turn Off | Idle Turn Off | Idle Turn off | Idle turn off |  |
| Regenerative Braking | Regenerative Braking14 | Regenerative Braking | Regenerative Braking | Regenerative Braking | Minimal Regen Braking | Regenerative Braking |  |
| Electric Only Drive | Electric Only Drive1 | Electric Only Drive | Electric Only Drive | Electric Only Drive | NO |  |  |
| Drivetrain Type3 | Likely Series/Parallel and/or Split16 | Series/Parallel & Split | Parallel | Parallel | Parallel | Parallel |  |
| Downsized Engine | Downsized Engine1 | Downsized Engine | Downsized Engine | Downsized Engine | NO | NO |  |
| Emissions: |  |  |  |  |  |  |  |
| Rating4 (Select Availability) | SULEV, likely AT-PZEV | SULEV/AT-PZEV expected | SULEV/AT-PZEV expected | SULEV/AT-PZEV expected |  |  |  |
| Rating4 (Nat’l Availability) |  |  |  |  |  |  |  |
| EPA Air Pollution Score5 |  |  |  |  |  |  |  |
| Annual Tailpipe CO218 | As low as 7,260 lbs | As low as 7,260 lbs |  |  | As low as 16,133 lbs |  |  |
| Annual CO2 Emissions6 | As low as 9,000 lbs | As low as 9,000 lbs |  |  | As low as 20,000 lbs |  |  |
| Total Annual GHG Emissions1, a |  |  |  |  |  |  |  |
| Power |  |  |  |  |  |  |  |
| Gas Engine1 | 4 cyl; 2.0L; 25hp1 |  |  |  |  | 4 cyl; 2.2L |  |
| Electric Motor | Two-25hp motors1 |  |  |  |  |  |  |
| Est. Combined hp |  |  |  |  |  |  |  |
| Battery | 300V Ni-MH (est)16 |  | Ni-MH | Ni-MH | 36V lead-acid | 36V lead-acid |  |
| CLEAR ACT |  |  |  |  |  |  |  |
| Technology Tax Credit17 |  |  |  |  |  |  |  |
| Performance Tax Credit17 |  |  |  |  |  |  |  |
| Other Notes | Expected to be quicker than conventional Saturn Vue1 | Gas engine for FWD; two separate electric motors to power front/rear wheels1 |  |  | Up to 20 kW generator capabilities1 | Belt starter generator system system |  |

|  | GM Silverado/Sierra & Tahoe/Yukon, Gen216 | Chevrolet Malibu16 | Ford Explorer16 | Toyota Camry16 | Dodge Durango16 |
| --- | --- | --- | --- | --- | --- |
| Model Year | 2007 | 2007 | Cancelled | ??? | Currently shelved |
| EPA Size Class1 | Fullsize Pickup | Midsize Sedan | Midsize SUV | Midsize sedan | Mid Size SUV |
| EPA Adjusted MPG City/Hwy2 | Potentially over 20 | Around 27 mpg |  |  | 22-30 |
| Combined MPG15 | Potentially over 20 |  |  |  | Up to 30 |
| Hybrid Technology: |  |  |  |  |  |
| Idle Turn Off | Idle Turn Off1 | Idle off | Idle Turn Off1 | Idle Turn Off |  |
| Regenerative Braking | Minimal Regen Braking1 | Minimal Regen Braking | Minimal Regen Braking | Regenerative Braking | Regenerative Braking |
| Electric Only Drive | NO |  | NO | Electric Only Drive | Electric Only Drive |
| Drivetrain Type | Parallel | Parallel | Parallel | Parallel | Split |
| Downsized Engine | NO | NO | NO | Downsized Engine | Downsized Engine |
| Emissions: |  |  |  |  |  |
| Rating4 (Select Availability) |  |  |  | SULEV/AT-PZEV expected |  |
| Rating4 (Nat’l Availability) |  |  |  |  |  |
| EPA Air Pollution Score5 |  |  |  |  |  |
| Annual Tailpipe CO218 |  | Around 10,755 lbs |  |  | As low as 13,200 lbs |
| Annual CO2 Emissions6 |  | Around 13,333 lbs |  |  | As low as 16,364 lbs |
| Total Annual GHG Emissions |  |  |  |  |  |
| Power |  |  |  |  |  |
| Gas Engine | 8 cyl; 5.3L; 285hp (est.) 11 |  |  |  | 6 cyl; 3.9L; 175hp |
| Electric Motor |  |  |  |  | 72hp |
| Est. Combined hp |  |  |  |  |  |
| Battery | ?? | 36V lead acid | 36V lead-acid | Ni-MH |  |
| CLEAR ACT |  |  |  |  | 20%-30%; $750 |
| Technology Tax Credit17 |  |  |  |  |  |
| Performance Tax Credit17 |  |  |  |  |  |
| Other Notes | Generator capabilities Integrated starter generator system | Belt starter generator system | Integrated starter generator system |  |  |

Other possible vehicles in the 2005-2010 timeframe with very little detail16:

Ford: Ford Freestyle crossover utility vehicle, Mercury and Mazda versions of the Escape, Ford Focus, Mercury Montego midsize luxury, Volvo XC90 mid-size SUV.

DaimlerChrysler: Chrysler Sebring midsize sedan, Dodge Caravan

Honda: Accord midsize sedan, Acura midsize sedan, Odyssey minivan, Pilot midsize SUV.

Nissan (using Toyota technology):  Altima midsize sedan, Quest minivan

Abbreviations:

Ni-MH – nickel metal hydride

LEV12 – Low Emission Vehicle:  weakest emission standard in California; 50% reduction in particulates and 66% reduction in nitrogen oxides compared to federal Tier II standard

ULEV12 – Ultra Low Emission Vehicle:  50% reduction in carbon monoxide when compared to LEV standard

SULEV12 – Super Ultra Low Emission Vehicle:  50% reduction in carbon monoxide and 70% reduction in nitrogen oxides when compared to ULEV standard

PZEV13 – Partial Zero Emission Vehicle:  same emissions standard as SULEV, but qualifying car must also have near-zero evaporative emissions and emissions control system must come with 150,000 mile/15 year warranty

# Notes

1. DeCicco, John, and James Kliesch.  ACEEE’s Green Book: The Environmental Guide to Cars & Trucks.  American Council for an Energy-Efficient Economy.  Washington, DC: 2003.

2. MPG City/Hwy is for automatic and CVT (continuously variable transmission) models.

3. Drivetrain classifications from UCS report:    Friedman, David.  A New Road: The Technology and Potential of Hybrid Vehicles.  Union of Concerned Scientists.  Cambridge, MA: 2003.

4. Emission Ratings & Availability:

Select: Vehicles are primarily available from dealers in CA, MA, ME, NY, VT and contiguous states including AZ, CT, NH, NJ, NV, OR, PA, RI.

National: Vehicles are generally available everywhere in the U.S.    http://www.fueleconomy.gov/feg/hybrid_sbs.shtml    http://www.epa.gov/autoemissions/all-rank-03.htm

5. vehicles are rated on a scale of 0-10 (10 being the cleanest) according to pounds of smog-forming pollution per 15,000 miles.

http://www.fueleconomy.gov/feg/hybrid_sbs.shtml    http://www.epa.gov/autoemissions/all-rank-03.htm

6. Annual CO2 Emissions calculated using (15,000 miles/year) / (Combined MPG) x (24 pounds CO2/gallon).  (includes upstream CO2 emissions and end-user CO2 emissions)

David Friedman, Senior Engineer, Union of Concerned Scientists:  personal communication 7/25/2003

7.  http://www.hondacars.com/models/model_overview.asp?ModelName=Civic+Hybrid

8. http://www.hondacars.com/models/model_overview.asp?ModelName=Insight

9. http://www.toyota.com/html/shop/vehicles/prius

10. http://www.auto123.com/en/info/news/previews,view,Toyota.spy?artid=13861&pg=1

11.  http://www.chevrolet.com/silverado

12.  www.dieselnet.com

13.  www.arb.ca.gov/msprog/ccbg/atpzev.htm

14.  http://www.saturnfans.com/Cars/Future/hybridvue.shtml

15. Combined MPG based on 55% city driving & 45% highway driving  http://www.environmentaldefense.org/tailpipetally/

16. David Friedman, Senior Engineer, Union of Concerned Scientists:  personal communication 7/25/2003

17. Tax credit figures derived from the CLEAR ACT (Senate Bill 505, 108th Congress) as drafted on March 4, 2003 http://frwebgate.access.gpo.gov/cgi-bin/getdoc.cgi?dbname=108_cong_bills&docid=f:s505is.txt.pdf

18. Tailpipe CO2 emissions calculated using (15,000miles/year)/(combined mpg) x (19.36 pounds CO2/gallon)   (only includes CO2 emitted from automobile tailpipe) - Lisa Snapp, EPA personal communication 8/5/2003

a.  Greenhouse gas emissions measured in tons per year.  These figures include embedded GHG emissions (those emitted during production of the vehicle), upstream GHG emissions (those emissions associated with the refining and transporting of gasoline), and end-user GHG emissions (those GHGs that actually leave the tailpipe of the car during driving).  The gases included in this measurement are converted to a CO2 equivalent (according to their “efficiency” in warming the atmosphere), and include carbon dioxide, hydrocarbons, nitrogen oxides, nitrous oxide, methane, and carbon monoxide.