Rhode Island Greenhouse Gas Baseline Scenario:

### Preliminary Figures and Tables

#### Prepared for

##### The Rhode Island Greenhouse Gas Policy Stakeholder Group

#### Prepared by

Alison Bailie, Steve Bernow, Rachel Cleetus,

Bill Dougherty, Charlie Heaps and Chella Rajan

Tellus Institute

11 Arlington Street

Boston, MA  02116

T: 617-266-540

Table of Contents

Overview	5

Summary Results	6

Appendix 1: Detailed Results	19

Appendix 2: Methodology, Assumptions and Data Sources	50

References	52

Table of Figures

Figure 1: Baseline Greenhouse Gas Emissions for Rhode Island: Total	5

Figure 2: Baseline Greenhouse Gas Emissions for Rhode Island: By Pollutant	6

Figure 3: Baseline Greenhouse Gas Emissions by Sector for Rhode Island	7

Figure 4: Baseline Greenhouse Gas Emissions by Sector for Rhode Island	8

Figure 5: Baseline Energy Sector Greenhouse Gas Emissions by Sector for Rhode Island	9

Figure 6: Baseline Electric/Fossil Greenhouse Gas Emissions by Sector	10

Figure 7: Residential Sector GHG Emissions By End Use	11

Figure 8: Commercial Sector GHG Emissions By Building Type	12

Figure 9: Transport Sector GHG Emissions: Passenger and Freight	13

Figure 10: Passenger Transport GHG Emissions by Mode	14

Figure 11: Industrial Sector GHG Emissions by Subsector	15

Figure 12: Electric Sector Energy GHG Emissions by Technology	16

Figure 13: Rhode Island Baseline GHG Emissions Compared to the New England Governors/ Canadian Premiere's Target	17

Figure 14: Baseline Greenhouse Gas Emissions for Rhode Island: Increase Since 1990	19

Figure 15: Growth in Greenhouse Gas Emissions since 1990	20

Figure 16: Energy Demand in 1999 by Sector and Fuel	21

Figure 17: Residential Sector GHG Emissions By Housing Type	22

Figure 18: Residential Sector GHG Emissions By End Use	23

Figure 19: Residential Sector Energy Consumption by End-Use (Final Energy Units)	24

Figure 20: Residential Sector Energy Consumption by Fuel (Final Energy Units)	25

Figure 21: Residential Sector Energy Consumption by End-Use (Primary Energy Units)	27

Figure 22: Residential Sector Energy Consumption by Fuel (Primary Energy Units)	28

Figure 23: Commercial Sector GHG Emissions By Building Type	29

Figure 24: Commercial Sector GHG Emissions By End Use	30

Figure 25: Commercial Sector Energy Consumption by End-Use (Final Energy Units)	31

Figure 26: Commercial Sector Energy Consumption by Fuel (Final Energy Units)	32

Figure 27: Commercial Sector Energy Consumption by End-Use (Primary Energy Units)	33

Figure 28: Commercial Sector Energy Consumption by Fuel (Primary Energy Units)	34

Figure 29: Freight Transport Emissions by Mode	35

Figure 30: Private Vehicles GHG Emissions: Cars vs Light Trucks and SUVs	36

Figure 31: Transport Sector Energy Demand by Fuel	37

Figure 32: Industrial Sector Energy Consumption by Subsector (Final Energy Units)	38

Figure 33: Industrial Sector Energy Consumption by Fuel (Final Energy Units)	39

Figure 34: Industrial Steam Production	40

Figure 35: Electric Sector Generation (GWhr)	41

Figure 36: Electric Sector Capacities	42

Figure 37: Nitrogen Oxide Emissions by Sector	43

Figure 38: Sulfur Dioxide Emissions by Sector	44

Figure 39: VOC Emissions by Sector	45

Figure 40: Partculate (PM10) Emissions by Sector	46

Figure 41: Summary of Residential Analysis Data Structure	47

Figure 42: Summary of Commercial Analysis Data Structure	48

Figure 43: Summary of Industrial Analysis Data Structure	49

Figure 44: Summary of Transport Analysis Data Structure	49

Figure 45: Summary of Energy Supply Analysis Data Structure	50

Figure 46: Summary of Non-Energy Sector Analysis Data Structure	50

# Overview

The sequence of figures that follows shows, with varying degrees of detail, the 1990-1999 history and the 1999-2020 Baseline forecast of Rhode Island’s GHG emissions.  The order of presentation introduces this information with increasing levels of detail, starting from the most aggregate (totals and sectoral splits) and moving towards disaggregated information (sub-sector and fuel use levels).  All historic data and forecast assumptions and results are mounted in the Tellus LEAP model.

The twelve (12) figures shown in here display Rhode Island’s GHG emissions in relatively aggregate form.  Note that total annual GHG emissions grow by 63 percent between 1990 and 2020.

The first three figures show (1) the total, (2) the total broken out into methane and forest emissions plus energy related emissions and (3) the total broken out into non-energy, energy supply (electricity and steam production) and energy demand (fossil fuel combustion in buildings, industry and transport).

Figure 4 shows the emissions baseline showing each sector that either consumes fossil fuels and emits GHGs, produces energy (electricity and steam) and emits GHGs, or emits GHGs from non-energy sources (solid waste and forests).

Figure 5 shows emissions from the energy related GHG emissions re-aggregated into the final demand sectors – residential, commercial, industry and transport – and including electricity in these sector totals insofar as they consume electricity.   Figure 6 breaks this up further into the fossil fuel and electricity contributions to emissions from each sector’s demand.

Figures 7 through 12, give the breakdown for each sector, into its sub-sectoral or end-use contributions – residential end-uses, commercial building types, transportation modes, industrial sub-sectors, electricity generation technologies.

We will post on the project website additional figures with still greater detail on GHG emissions and the energy uses and supplies that lead to these GHG emissions, along with the full structure of the Baseline modeling using the Tellus LEAP model.

The Baseline model was developed using the US Department of Energy (DOE) energy-use information for Rhode Island, plus its latest regional forecasts. The model takes account of economic, demographic, energy use and purchase, technology, and energy price information, based upon DOE’s integrated energy supply and demand model (the National Energy Modeling System), and economic and demographic conditions and evolution and climate data for Rhode Island.

# Summary Results

Figure 1: Baseline Greenhouse Gas Emissions for Rhode Island: Total

Figure 2: Baseline Greenhouse Gas Emissions for Rhode Island: By Pollutant

Figure 3: Baseline Greenhouse Gas Emissions by Sector for Rhode Island

Note that the non-energy sector is a small net sink (i.e. it removes carbon).

Figure 4: Baseline Greenhouse Gas Emissions by Sector for Rhode Island

Figure 5: Baseline Energy Sector Greenhouse Gas Emissions by Sector for Rhode Island

Notes:  This chart shows energy sector emissions with emissions from electric generation allocated among the four tertiary sectors (industry, transport, commerce and residential) based on the electricity consumed in those sectors.    Figure 3 below breaks these emissions out to show sectoral emissions from electricity and fossil fuel consumption separately for each sector

Figure 6: Baseline Electric/Fossil Greenhouse Gas Emissions by Sector

Figure 7: Residential Sector GHG Emissions By End Use

Figure 8: Commercial Sector GHG Emissions By Building Type

Figure 9: Transport Sector GHG Emissions: Passenger and Freight

Figure 10: Passenger Transport GHG Emissions by Mode

Figure 11: Industrial Sector GHG Emissions by Subsector

Figure 12: Electric Sector Energy GHG Emissions by Technology

Figure 13: Rhode Island Baseline GHG Emissions Compared to the New England Governors’/ Canadian Premiere's Target

# Appendix 1: Detailed Results

Figure 14: Baseline Greenhouse Gas Emissions for Rhode Island: Increase Since 1990

Figure 15: Growth in Greenhouse Gas Emissions since 1990

Figure 16: Energy Demand in 1999 by Sector and Fuel

Figure 17: Residential Sector GHG Emissions By Housing Type

Figure 18: Residential Sector GHG Emissions By End Use

Notes:  Emissions are dominated by single family dwellings (which increase in share over time from 71% of households in 1999 to 75% in 2020) and by water and space heating. Overall emissions growth is fairly low due to a combination of improvements in energy intensity and low overall population growth rates.  The population of RI is expected to increase from 991 thousand in 1999 to 1.1 million in 2020.  Notice that these charts do not include emissions from electricity consumed in the sector (see notes that follow).

Figure 19: Residential Sector Energy Consumption by End-Use (Final Energy Units)

Figure 20: Residential Sector Energy Consumption by Fuel (Final Energy Units)

Household energy consumption is dominated by energy used for space and water heating and by the fuels natural gas, fuel oil and electricity, and to a lesser degree wood.  However, this picture is misleading from an emissions perspective since it undercounts the fuels used in generating electricity.  Figure 21and  Figure 22 respectively redisplay these same charts, with electricity consumption counted in primary energy equivalent units (i.e. the amount of primary energy required to generate a unit of electricity).  In New England 1 GJ of electricity consumed requires that 4 GJ of primary energy be consumed in electric generation).

Figure 21: Residential Sector Energy Consumption by End-Use (Primary Energy Units)

Figure 22: Residential Sector Energy Consumption by Fuel (Primary Energy Units)

Notes:  When redisplayed in primary energy equivalent units, residential electricity consumption appears much more important, as do electric appliances and space cooling.

Figure 23: Commercial Sector GHG Emissions By Building Type

Figure 24: Commercial Sector GHG Emissions By End Use

Figure 25: Commercial Sector Energy Consumption by End-Use (Final Energy Units)

Figure 26: Commercial Sector Energy Consumption by Fuel (Final Energy Units)

Figure 27: Commercial Sector Energy Consumption by End-Use (Primary Energy Units)

Figure 28: Commercial Sector Energy Consumption by Fuel (Primary Energy Units)

Figure 29: Freight Transport Emissions by Mode

Figure 30: Private Vehicles GHG Emissions: Cars vs Light Trucks and SUVs

Figure 31: Transport Sector Energy Demand by Fuel

Figure 32: Industrial Sector Energy Consumption by Subsector (Final Energy Units)

Figure 33: Industrial Sector Energy Consumption by Fuel (Final Energy Units)

Figure 34: Industrial Steam Production

Figure 35: Electric Sector Generation (GWhr)

Figure 36: Electric Sector Capacities

Figure 37: Nitrogen Oxide Emissions by Sector

Figure 38: Sulfur Dioxide Emissions by Sector

Figure 39: VOC Emissions by Sector

Figure 40: Partculate (PM10) Emissions by Sector

Figure 41: Summary of Residential Analysis Data Structure

Figure 42: Summary of Commercial Analysis Data Structure

Figure 43: Summary of Industrial Analysis Data Structure

Figure 44: Summary of Transport Analysis Data Structure

Figure 45: Summary of Energy Supply Analysis Data Structure

Figure 46: Summary of Non-Energy Sector Analysis Data Structure

# Appendix 2: Methodology, Assumptions and Data Sources

The figures and tables presented in this report are the result of taking the historical pattern of emissions for greenhouse gases (GHGs) and criteria air pollutants (CAPs) from Rhode Island (RI), and projecting emissions forward until 2020 based on assumptions about how energy intensities, emission factors and overall macroeconomic and demographic factors are likely to evolve in the future.  The base year for the analysis was 1999: the most recent year for which a generally consistent set of data could be gathered.  Hence the term “future” refers to emissions for any year after 1999.

In analyzing RI’s greenhouse gas emissions, the availability of data is a serious constraint.  In particular, there is little available information about the detailed structure of energy consumption for RI.  We have therefore generally based our analysis of future emissions on energy intensity forecasts (BTU per unit of activity) for the Northeastern United States as a whole, available in the EIA’s National Energy Modeling System (NEMS), coupled with RI-specific estimates of activity levels in each sector/subsector.

- In the residential sector we coupled New England-specific energy intensities from NEMS (in BTU per household) for the various different end-uses (cooking, heating, lighting space cooling, etc.) differentiated by household type (single family, multi-family and mobile home dwellings) with RI-specific estimates of the number of households (from the U.S Census Bureau) and NEMS data for the fraction of each household type for New England.  Future fuel shares, energy intensities and households growth were taken from NEMS results for New England.  Fossil fuel emission factors in the sector (lb/mmBTU) for 1999 were based on data in the EPA’s National Air Quality and Emissions Trends Report 1999, and were assumed to remain constant in the future.

- In the commercial sector we used New England energy intensities for the various end uses in each major building type (offices, hospitals, warehouses, non-building energy use, etc.) for 1999 from NEMS (in BTU per square foot of floor space) coupled with RI-specific estimates of floor space for each major commercial subsector (NEMS data scaled to RI based on RI GSP data from BEA).  The growth in floor space, future energy intensities, and fuel share trends after 1999 were all taken from NEMS results for New England.  Fossil fuel emission factors in the sector (lb/mmBTU) for 1999 were based on data in the EPA’s National Air Quality and Emissions Trends Report 1999, and were assumed to remain constant in the future.

- In the industrial sector we coupled Northeastern energy intensities for fuel use (BTU per dollar value of output) in each major sector (chemicals, construction, food processing, non-intensive industries, etc.) with RI-specific estimates of value of output from each sector (U.S. census bureau).  The growth in value of output, future energy intensities, and fuel share trends after 1999 were all taken from NEMS results for the Northeast.  Fossil fuel emission factors in the sector (lb/mmBTU) for 1999 were based on data in the EPA’s National Air Quality and Emissions Trends Report 1999, and were assumed to remain constant in the future.

- Emissions from the transport sector in 1999, were based on regional transportation fuel use statistics for RI from the EIA SEDR.  Total SEDR fuel use allocated to the various transportation modes using data from the Federal Highway Authority and the EIA (AEO2001).  Energy intensities (fuel economy) were taken from a recent Tellus study, which in turn is based on data from the EIA and Oak Ridge National Laboratory.    Estimates of vehicle miles traveled (VMTs) in 1999 for each mode were calculated based on the above levels of total energy use and fuel economy.  Finally, VMTs were translated into passenger and freight transport service requirements (passenger-miles and ton-miles), which are a better overall indicator of overall transportation service requirements, using load factor data for each technology developed for a recent Tellus study.  Future passenger light duty vehicle VMTs were assumed to grow in line with overall population growth.  VMT growth in other modes was assumed to equal to overall growth in Gross State Product (GSP).  Load factors were assumed to remain constant.  Fuel economy improvements and modal shifts (e.g. from cars to SUVs) are assumed to be in-line with EIA projections.  Transport sector emission factors are based on a Tellus institute model that uses a stock turnover model for New England to examine how new vehicle emissions regulations are translated into future average emission factors.

- Emissions from electricity consumption were derived from the electricity consumption levels calculated for each demand sector.  These are assumed to be met by the New England generating pool as a whole.  Hence, electricity generation was modeled by allocating a fraction of the overall capacity of New England to RI.  The fraction was RI’s share of total New England electricity sales (6% in 1999).  Information on the current and future mix of power plants in the New England pool was taken from NEMS, as were future levels of transmission and distribution losses.  Emission factors (lb/mmBTU of feedstock fuel) for 1999 were based on data in the EPA’s National Air Quality and Emissions Trends Report 1999, and were assumed to remain constant in the future.   Future power plant efficiencies, capacity factors and other technical information were taken from NEMS results for the New England power pool.

- Non energy sector emissions are negligible compared to those in the energy sector.  This analysis assumed the same level of non-energy sector emissions calculated for the recent Brown University Inventory of Greenhouse Gas Emissions for 1996.  Future emissions levels are assumed to remain constant.

In each demand sector, calculated base year energy consumption patterns for each fuel (in 1999) were calibrated to match energy consumption statistics for the State contained in the EIA’s State Energy Data Report (SEDR).   The above calculations were calibrated by adjusting the energy intensity values from NEMS for the base year and all future years.  This calibration presumably reflects differences in the fuels and technologies used in a given subsector between RI and New England, but may also reflect differences in data definition, differences in the structure of production and consumption in each subsector, or problems with the EIAs state energy statistics.

# References

Bureau of Economic Analysis.  2001.  Regional Accounts Data.   U.S. Department of Commerce.  http://www.bea.doc.gov/bea/regional/data.htm

United States Environmental Protection Agency.   National Air Quality and Emissions

Trends Report, 1999  http://www.epa.gov/ttn/chief/trends/index.html

United States Department of Energy, Energy Information Administration (DOE/EIA).  2001. Annual Energy Outlook 2001 With Projections to 2020. http://www.eia.doe.gov/oiaf/aeo/   Report#:DOE/EIA-0383(2001).

United States Department of Energy, Energy Information Administration (DOE/EIA).  2000. National Energy Modeling System.  http://www.eia.doe.gov/oiaf/aeo/overview/index.html   Report#:DOE/EIA-0581(2000)

Brown University and Rhode Island Department of Environmental Management. 2000. Rhode Island Greenhouse Gas Emissions Inventory.  http://www.brown.edu/Research/EnvStudies_Theses/GHG/index.shtml

United States Department of Energy, Energy Information Administration (DOE/EIA).  2001. Sate Energy Data Report. http://www.eia.doe.gov/emeu/states/main_ri.html

Oak Ridge National Laboratory.  2000. Transportation Energy Data Book. Edition 20. http://www-cta.ornl.gov/data/tedb20/ ORNL-6959 (Edition 20 of ORNL-5198)

Office of Highway Policy Information, Federal Highway Administration.  1999. Highway Statistics. http://www.fhwa.dot.gov/ohim/hs99/index.htm

# Footnotes

NEMS is the Federal Government’s official energy forecasting model and is used primarily to produce the EIA’s Annual energy outlook publication, which forecasts energy demand and supply over a 20 year period.