# Rhode Island Greenhouse Gas Revised Baseline Scenario:

### Extended Figures and Tables

#### Prepared for

##### The Rhode Island Greenhouse Gas Policy Stakeholder Group

#### Prepared by

Alison Bailie, Steve Bernow, Rachel Cleetus,

Bill Dougherty, Charlie Heaps and Chella Rajan

Tellus Institute

11 Arlington Street

Boston, MA  02116

1/24/2002

Figure A: Baseline Greenhouse Gas Emissions for Rhode Island: Increase Since 1990 (Carbon Equivalent)

Figure B: Growth in Greenhouse Gas Emissions since 1990

Figure C: Energy Demand in 1999 by Sector and Fuel

Figure D: Residential Sector GHG Emissions By Housing Type

Figure E: Residential Sector Energy Consumption by End-Use (Final Energy Units)

Figure F: Residential Sector Energy Consumption by Fuel (Final Energy Units)

Household energy consumption is dominated by energy used for space and water heating and by the fuels natural gas, fuel oil and electricity, and to a lesser degree wood.  However, this picture is misleading from an emissions perspective since it undercounts the fuels used in generating electricity.  Figures G and H respectively redisplay these same charts, with electricity consumption counted in primary energy equivalent units (i.e. the amount of primary energy required to generate a unit of electricity).  In New England 1 GJ of electricity consumed requires about 4 GJ of primary energy be consumed in electric generation).

Figure E1: Residential Sector Energy Consumption by End-Use (Primary Energy Units)

Notes:  When redisplayed in primary energy equivalent units, residential electricity consumption appears much more important, as do electric appliances and space cooling.

Figure F1: Residential Sector Energy Consumption by Fuel (Primary Energy Units)

Figure G: Commercial Sector GHG Emissions By End Use

Notes:  Space and water heating are again important in the commercial sector.

Figure H: Commercial Sector Energy Consumption by End-Use (Final Energy Units)

Figure I: Commercial Sector Energy Consumption by Fuel (Final Energy Units)

Figure H1: Commercial Sector Energy Consumption by End-Use (Primary Energy Units)

Figure I1: Commercial Sector Energy Consumption by Fuel (Primary Energy Units)

Figure J: Freight Transport Emissions by Mode (Carbon Equivalent)

Figure K: Private Vehicles GHG Emissions: Cars vs Light Trucks and SUVs

Figure L: Transport Sector Energy Demand by Fuel

Figure M: Industrial Sector Energy Consumption by Subsector (Final Energy Units)

Figure N: Industrial Sector Energy Consumption by Fuel (Final Energy Units)

Figure O: Industrial Steam Production

Figure P: Electric Sector Generation (GWhr)

Figure Q: Nitrogen Oxide Emissions by Sector

Figure R: Sulfur Dioxide Emissions by Sector

The temporary increase over the years 2010-2020 is largely due to the phase-out of some nuclear power, and the consequent increased reliance on fossil fuels.

Figure S: VOC Emissions by Sector

Figure T: Partculate (PM10) Emissions by Sector

Figure U: Summary of Residential Analysis Data Structure

Figure V: Summary of Commercial Analysis Data Structure

Figure W: Summary of Industrial Analysis Data Structure

Figure X: Summary of Transport Analysis Data Structure

Figure Y: Summary of Energy Supply Analysis Data Structure

Figure Z: Summary of Non-Energy Sector Analysis Data Structure