# Rhode Island Greenhouse Gas 
Policy Scenarios

### Selected Figures

#### Prepared for

##### The Rhode Island Greenhouse Gas Policy Stakeholder Group

#### Prepared by

Alison Bailie, Steve Bernow, Rachel Cleetus,

Bill Dougherty, Charlie Heaps and Chella Rajan

Tellus Institute

11 Arlington Street

Boston, MA  02116

6/05/02

Figures

Figure 1: Rhode Island GHG Emissions Scenarios Compared to Governors’/Premiers’ Target	7

Figure 2: Contribution of Measures to Scenario: High, Medium and Non-Consensus/All	8

Figure 3: Components of Cumulative GHG Savings in Scenario High, Medium and Non-Consensus/All vs. Baseline	9

Figure 4: Scenario Benefits vs. GHG Savings	10

Figure 5: Net Costs and Benefits of Scenarios vs. Baseline	11

Figure 6: NOx Emissions from Scenarios	12

Figure 7: VOC Emissions from Scenarios	12

Figure 8: PM10 Emissions from Scenarios	13

Figure 9: SO2 Emissions from Scenarios	13

###### Overview of Scenario Analysis

The figures included in this summary are the key results of an analysis in which the various Working Group options have been modeled within the LEAP energy modeling framework to analyze their combined energy and greenhouse gas savings potential and their economic costs and benefits versus the baseline scenario (which has been described in an earlier memo).

Tellus grouped the options into one of the following six scenarios, based on the earlier “binning” of options by the Working Groups.  Tellus developed a seventh scenario (for saved carbon only) that included all of the options in Scenario 6 above plus the low priority options identified by the Working Groups and the non-binned option identified by the Transport and Land-use Working Group: VMT-based car insurance

- High priority options requiring action within the State only.

- High priority options requiring action both within and beyond the State.

- High & medium priority options requiring action within the State only.

- High & medium priority options requiring action both within and beyond the State.

- High & medium priority and non-consensus options requiring action within the State only.

- High & medium priority options requiring action both within and beyond the State.

- High, medium & low priority options requiring action both within and beyond the State

Note that only 3 options are assumed to require action beyond the State level:

- Buildings and Facilities Option 3.1: Appliance efficiency standards

- Energy Supply and Solid Waste Option 2.2: Carbon cap and trade

- Transport and Land-Use Option 1.1.1: National CAFE standard

Tellus entered the following information for the measures listed in Table 1 into LEAP:

- energy and/or GHG savings potential of the measure versus the Baseline scenario (as developed for the earlier scoping papers)

- unit costs of saved energy of demand-side options

- capital and operating and maintenance (O&M) costs of electric generation technologies

- unit prices of the various fuels consumed in Rhode Island.

Tellus then used LEAP to combine the options into the seven scenarios and to compare and contrast the effect of the different scenarios. All of the demand-side measures are assumed to be additive. Each scenario results in significant reductions in electricity generation requirements. Moreover, each of the scenarios includes a Renewable Portfolio Standard (RPS), which specifies that by 2020, non-hydro renewables should account for 20% of electricity generation.  To model these situations, we used the U.S. DOE’s National Energy Modeling System (NEMS) to examine what types of power plants will be avoided in New England in future scenarios with lower electric demand growth.  NEMS simulates that virtually all of the reductions in generation will be due to avoided Natural Gas Combined Cycle power plants.  The corollary of this is that none of the scenarios show significant differences in emissions from coal and oil-fired generation.  We also used NEMS to examine what types of power plants are likely to be used to meet the RPS. The types of plants used vary over time as Wind and Biomass technologies become more economic and as Municipal Solid Waste becomes more fully utilized.  By 2020, the RPS is generated from approximately 43% biomass, 33% Wind and 25% Municipal Solid Waste..   The results of the analysis in NEMS were entered into LEAP, which was then used to examine the overall costs, and emissions implications of each integrated scenario.

## Table 1: Scenario Options

Building & Facilities Working Group

| Consensus Options High Priority |
| --- |
| 2.6 | Energy efficiency in existing nonresidential facilities: implement substantial new fossil-oriented program. |
| 3.1 (Federal) | Upgrade and extend appliance efficiency standards |
| 5.2 | Compact appliances life style option |
| 6.2 | Energy efficiency targets adopted by industrial firms |
| 4.1 | Combined heat & power (CHP) in industry |
| 1.6 | Electric energy efficiency in existing nonresidential facilities: extend “Energy Initiative” |
| 6.3 | Reinstate and expand tax credits, for energy efficiency |
| 4.2 | CHP in buildings and facilities (non-industrial) |
| 2.1 | Efficient residential electric cooling initiative |
| 1.3 | Retrofit program for electrically heated homes |
| 2.5 | Retrofit program for fossil heated homes |
| 1.2 | Efficient lighting and efficient appliances DSM programs |
| 1.5 | “Design 2000” DSM for efficient new nonresidential construction |
| 1.4 | “Energy Star” DSM for efficient new residential construction |
| 1.7 | Small commercial & industrial DSM program |
| 6.1 | Public facilities efficiency initiative |
| 2.4c | Encourage use of lower carbon fossil fuels |
| Medium Priority |
| 2.2 | Efficient residential fossil fuel heating initiative |
| 5.1 | Compact floor space life style option |
| Low Priority |
| 2.4b | Switching from electricity to fossil fuel heating |
| 1.1 | Solar PV buy-down program |
| 2.3 | Active solar hot water heating program |
| 2.7 | Nonresidential gas air conditioning |
| Non-Consensus |
| 3.2a | Upgrade new residential construction building code |
| 3.2b | Upgrade new commercial construction building code |
| 2.4a | Switching from oil to natural gas |

## Energy and Solid Waste Working Group

| Consensus Options |
| --- |
| High Priority |
| 3.1 | Pay-As-You-Throw |
| 3.3 | Resource management contracting |
| 1.3 | Renewable portfolio standard |
| 2.2 (Federal) | Carbon cap and trade permit system |
| Medium Priority |
| 1.5 | Direct investments or expenditures |
| 1.1 | SBC - supply options |
| 1.6 | State Facilities Renewable Purchase Requirement |
| 1.1 | SBC - demand options |
| 1.2.1, 1.2.2 1.4 | Incentive Package (Production tax credit, investment tax credit, net metering, backup rates) |
| Low Priority |
| 3.5 | Deposit bottle system (“bottle bill”) |

Transportation and Land Use Working Group

| High Priority |
| --- |
| 1.1.1 (Federal) | National CAFÉ standards |
| 3.1.1 | Urban/Suburban Forestry |
| 3.1.2 | Continuation of Open Space Protection |
| 1.1.2 | Fuel economy improvements, using local initiatives |
| 2.1 | Transit oriented development and enhancing transit options and operations |
| 2.2 | Expand bicycle and pedestrian infrastructures |
| 2.3 | Commuting efficiency |
| 2.4 | Reducing commuting trips |
| 1.2 | Government-owned vehicle carbon efficiency |
| Low Priority |
| 3.3.1 | Conversion of Marginal Cropland to Forest |
| 4.2 | Fleet fuel GHG content mandate |
| 3.3.2 | Conversion of Marginal Cropland to Wetlands |
| 3.3.4 | Low Input Agriculture and Improved Cropping Systems |
| Non-Consensus Option |
| 1.3 | Increase the gasoline tax |
| Agreed to Research but Not to Bin Now |
| 1.4 | Create VMT-based insurance premium structures |

Figure 1: Rhode Island GHG Emissions Scenarios Compared to Governors’/Premiers’ Target

This “jaws” chart shows the GHG emissions trajectory of each of the seven scenarios along with the targets adopted recently by the New England Governors/Canadian Premieres conference.  Notice that only two scenarios meet or exceed the target: High/Medium & Non-Consensus/All (HMNA) and the HMNA plus the Low Priority Options.  The values combine emissions from all greenhouse gases tracked in the LEAP scenarios including carbon dioxide and methane, and combine them based on their overall global warming potential (GWP).  Thus the units are tonnes of carbon equivalent.

Figure 2: Contribution of Measures to Scenario: High, Medium and Non-Consensus/All

This chart shows how the three groups of measures identified by each working group contribute to the overall GHG emissions savings of the scenario High, Medium and Non-Consensus/All versus the Baseline scenario.

Figure 3: Components of Cumulative GHG Savings in Scenario High, Medium and Non-Consensus/All vs. Baseline

This chart shows the contribution to the cumulative GHG savings in scenario High, Medium and Non-Consensus/All from each of the measures.  Notice that the two largest measures: national CAFÉ standards, and appliance efficiency standards measures are both federal measures.  These account for approximately 27% of all cumulative GHG savings.  The top ten measures in terms of GHG savings account for 69% of cumulative GHG savings.

Figure 4: Scenario Benefits vs. GHG Savings

This chart shows the cumulative GHG savings and the cumulative discounted net economic benefits (i.e. benefits minus costs) through 2020 of each scenario versus the Baseline.  Note that costs are only assessed through 2020, not through each measure’s entire lifetime. There will therefore be additional benefits beyond 2020 for things installed before 2020 that are still functioning and saving, which are not included here.

Note also that the more aggressive scenarios actually yield more economic benefits. Economic costs and benefits have not been quantified for the final scenario, which includes low priority options.

Figure 5: Net Costs and Benefits of Scenarios vs. Baseline

Chart shows the cost and benefit components of each of the six main scenarios.  Costs are the additional capital and O&M costs of purchasing and using more expensive energy efficient equipment (mainly in the transport sector and in buildings and facilities), while benefits are (a) the avoided costs of fuel that no longer needs to be purchased in the scenario (compared to the fuel that would have been purchased in the Baseline scenario); (b) avoided environmental externality costs due to the lower level of non-greenhouse gas air pollutant emissions in the policy scenarios compared to the Baseline scenario.  Externalities values are based on a review of externality values that have been adopted or proposed by State Public Utility Commissions for use in electric power planning.  Note that capital and O&M costs for electric power generation are too small to appear on this chart.  This is because the additional costs of purchasing and operating more expensive renewables are balanced by the benefits of the combined cycle natural gas power plants that are avoided because of the lower electricity demands in the scenarios.

Figure 6: NOx Emissions from Scenarios

Figure 7: VOC Emissions from Scenarios

Notes:

In Figure 6, High/State and High &Medium/State are virtually identical, and High/All and High & Medium/All are virtually identical.

In Figure 7, High/State and High &Medium/State are virtually identical, and High/All and High & Medium/All are virtually identical.

Nitrogen oxides (NOx) form when fuel is burned at high temperatures, as in a combustion process. NOx is involved in the formation of ground-level ozone, which can trigger serious respiratory problems. It reacts to form nitrate particles, acid aerosols, as well as NO2, which also cause respiratory problems.  It also contributes to formation of acid rain and to nutrient overload that deteriorate water quality.  NOx  also contributes to atmospheric particles that cause visibility impairment most noticeable in national parks, and reacts to form toxic chemicals. It also

contributes to global warming. (summarized from EPA web site: http://www.epa.gov/air/urbanair/nox/index.html)

Volatile Organic Compounds contribute to the production of photochemical smog and to ground level ozone, which affects the human respiratory system. High ozone levels can also damage crops, forests and wildlife (summarized from “a Guide to Environmental Analysis for Energy Planners: http://www.tellus.org/seib/publications/emanual.pdf)

Figure 8: PM10 Emissions from Scenarios

Figure 9: SO2 Emissions from Scenarios

In Figure 8,  High/State and High &Medium/State are virtually identical, and High/All and High & Medium/All are virtually identical.

In Figure 9, High/All and High & Medium/All are virtually identical.

Particulate matter of size less than 10 microns in diameter (PM10).  Particulates are associated with serious health effects including increased hospital admissions and emergency room visits for people with heart and lung disease, and work and school absences. Particulates are the major source of haze that reduces visibility in many parts of the United States, including National Parks. Particulates settle on soil and water and harm the environment by changing the nutrient and chemical balance. They also cause erosion and staining of structures.  (Summarized from EPA web site: http://www.epa.gov/ebtpages/airairposulfuroxidesso2.html)

Sulfur Dioxide (SO2) is formed when fuels containing sulfur, such as coal and oil are burned.  SO2 contributes to respiratory illness, particularly in children and the elderly, and aggravates existing heart and lung diseases. It contributes to the formation of acid rain, which damages trees, crops, historic buildings, and monuments; and makes soils, lakes, and streams acidic. It also contributes to the formation of atmospheric particles that cause visibility impairment, most noticeably in national parks. (summarized from EPA web site: http://www.epa.gov/ebtpages/airairposulfuroxidesso2.html)

# Text boxes

See Figure 5 for details of benefits

“All Other” Measures

Efficient Heating Initiative

Efficient Residential Cooling

Building Shell Retrofit--Electricity

Tax Credits for Energy Efficiency

Design 2000

Efficient Lighting & Appliances

Building Shell Retrofit--Fossil

Compact Floor Space

Public Facilities Initiative

Design 2000

Energy Star Homes

State Incentives for Fuel         Economy

Local Govt. Vehicle Fuel Efficiency

Fuel Switch Oil to Gas

Thousand Tonnes